SIR C.R.R COLLEGE OF ENGINEERING

DEPARTMENT OF MECHANICAL ENGINEERING

IV/IV, SEC-A& B	      ACADEMIC YEAR: 2015-16		Dt: 23/09/15

SQC ASSIGNMENT-II

BATCH 1

BATCH 2

BATCH 3

BATCH 4

BATCH 5

BATCH-6

- Write a short notes on

- Quality costs.

- Rectifying inspections.

- Type 1 and type 2 error in control charts.

- Write a short notes on np charts? Discuss.

- Give the comparison between attribute control charts & variable control charts.

- 10 samples of each 50 size of a pipe were inspected in pressure testing. The results of the inspection are some as below.

| Sample No | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| No of Defectives | 2 | 3 | 2 | 1 | 2 | 3 | 2 | 1 | 2 | 3 |

- Write a Short notes on

- Type 1 and type 2 errors of the control charts.

- Demerit rating.

- What is multiple sampling? What are its disadvantages?

- Define tolerance fit. What is its use in process capability analysis?

- A machine is manufacturing mica discs with specified thickness between 0.008” and 0.015” samples of size 4 are drawn every hour an their thickness in units

(1 unit = 0.001”) are recorded as follows:

| Sample No | Thickness of mica discs (1unit = 0.001”) |
| --- | --- |
| 1 | 14 | 8 | 12 | 12 |
| 2 | 11 | 10 | 13 | 8 |
| 3 | 11 | 12 | 16 | 13 |
| 4 | 15 | 12 | 14 | 11 |
| 5 | 10 | 10 | 8 | 8 |

For the above data, setup an R-Chart and an X-Chart. Plot the observed points and comment on the same

- What is quality loss?

- What is off-line quality control?

- What are type 1 errors?

- Explain the use of control charts?

- Explain the nominal type of product specification.

- What is the use of a p-chart?

- What is process capability ratio?